## Slide 1
Dagmawi Abera
Hamede Abdulgafur
Noah Awol
PROJECT
SMART MIRROR
FINAL PRESENTATION
THE QUANTUM ALCHEMISTS :

## Slide 2
TABLE OF CONTENTS
  Introduction to the Smart Mirror Project
  System Level drawing/ Block Diagram
  Technical Details
  Final Results and Achievements
  Problem Faced and Overcome
  Current and Future Work
  Updated Gantt Chart

## Slide 3
INTRODUCTION TO THE SMART MIRROR PROJECT
Context and Overview
In today's digital era, there's a growing need to enhance everyday objects with technology. The Smart Mirror project transforms the traditional home mirror into an interactive device, merging aesthetics with functionality. This advanced mirror displays real-time information like weather, news, and calendar events, and personalizes content for individual users.
Goals of the Smart Mirror
  Functionality: Enhance mirrors to display relevant real-time information seamlessly.
  Personalization: Enable custom profiles to cater to individual user preferences.
  User Experience: Offer an intuitive interface that simplifies access to desired information with minimal interaction.
Implementation Strategy
Our strategy involves integrating a high-definition display and sensors into a two-way mirror, developing user-friendly software that pulls real-time data.

## Slide 5
TECHNICAL DETAILS
  Magic Mirror Platform: We used Magic Mirror², an adaptable open-source platform that allows for extensive customization through modular additions.
  Custom Software Modules:
    Spotify Integration: Developed a custom module to integrate Spotify using its API, enabling direct music streaming and user interaction within the mirror interface.
    PIR Sensor Management: Custom script written to interface with the PIR motion sensor, managing the display's power state by turning it off during inactivity and reactivating upon motion detection.
    Voice Command Integration: Integrated Google Assistant via a mini microphone setup, allowing for voice-controlled interactions and responses, enhancing user convenience.
  User Interface Enhancements:
    Implemented interactive features such as real-time news updates, weather forecasts, and personal greetings, each through respective modules that fetch and display dynamic content based on user preferences and environmental data.

## Slide 6
FINAL RESULTS AND ACHIEVEMENTS
  Successful Hardware Integration: Overcoming initial challenges, our team, Dagmawi and Noah, successfully integrated all hardware components essential to our project's foundation.
  Software Development Completion: Under the leadership of Hamede Abdulgafur, we completed the integration of crucial software modules, ensuring a seamless and functional application environment.
  Enhanced Display Environment for Smart Mirror: Our Smart Mirror now boasts a comprehensive display environment designed to enhance daily routines. Key features include:
    Google Calendar integration
    Personalized greetings and compliments
    Access to recent news
    Displays of current time and weather
    Future weather forecasts
    Spotify integration with custom API for music streaming

## Slide 7
New Sensor and Audio Implementations:
  PIR Body Motion Sensor: We've added a PIR Body Motion Sensor, enhancing user interaction by detecting presence effectively. We've set a threshold of 2 minutes; if no motion is detected within this time, the display will automatically turn off. The display will reactivate once motion is detected again.
  Mini Microphone for Raspberry Pi: Integration of a mini microphone has been successful, enabling voice commands and interactions.
  Speaker Functionality: After addressing an initial issue where the speaker wire was connected inversely to the motherboard of the display monitor, our speaker is now fully operational. We confirmed that both Google Assistant responses and Spotify streaming are working flawlessly
FINAL RESULTS AND ACHIEVEMENTS
MINI PIR Motion sensor
Microphone

## Slide 8
Enhancements in Hardware Management:
  Raspberry Pi Case with Cooling Fan: we purchased a case equipped with a cooling fan for our Raspberry Pi. This decision ensures that the device remains cool and functional, as it operates continuously within our Smart Mirror setup.
  Aesthetic and Protective Covering: To enhance the visual appeal and protect the internal components, we've covered the back of our Smart Mirror with a black sheet. This not only improves the aesthetic but also conceals the inner workings, ensuring a sleek and tidy appearance.
FINAL RESULTS AND ACHIEVEMENTS

## Slide 10
FUTURE DIRECTIONS AND FURTHER IMPROVMENTS
  Motion Sensor Placement: Plan to embed the PIR motion sensor directly behind the mirror for improved responsiveness and a cleaner design.
  Advanced Voice Interaction: Enhance voice command capabilities with more sophisticated processing for complex interactions.
  User Customization: Develop an interface for personalized settings, allowing users to adjust display and module preferences.
  Health and Wellness Modules: Integrate health-focused features to provide reminders and fitness tracking directly on the mirror.
  Energy Management: Implement smarter protocols to optimize energy use based on user habits and environmental cues.

## Slide 11
Yes
UPDATED GANTT CHART

## Slide 12
THANK YOU!